## Slide 1: AHB UART Peripheral

## Slide 2: Building a System on a Chip (SoC)
Memory
VGA
Peripheral
UART
Peripheral
Timer
Peripheral
GPIO
Peripheral
7-Segment
Peripheral
Arm CMSIS-Core
Application Programming Interface (API)
Application Design (e.g., Game)
Arm Cortex-M0
Processor
Hardware design
Software low-level drivers & libraries programming
Software high-level
application development
Peripheral Drivers
AHB
Notes: This module explores how to connect our SoC to a computer in order to exchange data. For this, we will use the Universal Asynchronous Receiver/Transmitter (UART) protocol.

## Slide 3: Serial Communication
  Serial Communication
  Transmits data one bit at a time in a sequential fashion
  Commonly used for long-haul communication, modems, and non-networked communication between devices
  Example are UART, SPI, I2C, USB, Ethernet PCI Express, etc.
1
0
1
1
1
0
0
1
1
0
1
1
1
0
0
1
Serial communication
Notes: Digital data communication occurs in two basic modes: serial or parallel. The type of transmission mode to be used depends on the wire length required by the communication bandwidth.
In serial transmission, bits are sent sequentially on the same line. This reduces the wiring costs but also slows the communication speed. Serial transmission is commonly used for long-haul communication, modems, and non-networked communication between devices.
Examples of serial mode transmission include connections between a computer and a modem using the RS-232 protocol. Other serial transmission protocols include UART, SPI, I2C, USB, and Ethernet PCI Express.

## Slide 4: Types of Serial Communication
Synchronous serial transmission
  A common clock is shared by both the sender and the receiver.
  More efficient transmission, since one wire is dedicatedly used for data transfer
  More costly, since an extra clock wire is required
Asynchronous serial transmission
  The sender does not have to send a clock signal.
  Both the sender and receiver agree on timing parameters in advance.
  Special bits are added to synchronize transmission.
Notes: Serial communications can be either synchronous or asynchronous. In synchronous serial transmission, data transmission is synchronized using a clock signal. Extra wiring is needed in order to distribute the clock signal. In asynchronous transmission, data transmission is coordinated using handshake protocols, which indicate the start and end of the transmission. This means there is no need for the clock signal to be transmitted; however, both the transmitter and receiver will need to agree on how to coordinate data transfer (e.g., baud rate). Asynchronous transmission allows for arbitrary size gaps between frames.
Asynchronous data transmission typically needs more than one wire per data item, as opposed to one wire in the case of synchronous transmission.

## Slide 5: UART Overview
UART
  Asynchronous communication, no clock wire required, pre-agreed baud rate
  Separate transmission and receiving wires
UART communication
  Converts data from parallel to serial
  Sequential data is transferred through serial cable
  Receives the sequential data and reassembles it back to parallel
Device 1
tx
tx
rx
Device 2
rx
tx
Notes: A UART is a piece of hardware that converts data from serial to parallel and vice versa. It uses asynchronous communication between sender and receiver with a pre-agreed baud rate, wherein the communication link has separate transmission and receiving wires. The sender converts data from parallel to serial, which is transferred through a serial cable. The receiver reassembles data back to parallel. One typical application of UART is the connection of a piece of hardware (e.g., modem) to a computer.

## Slide 6: UART Protocol
Data transfer starts with a starting bit by driving logic to low for one clock cycle.
In the next eight clock cycles, eight bits are sent sequentially from the transmitter.
Optionally, one parity bit can be added to improve transfer reliability.
In the end, the data wire is pulled up high to indicate completion of the transfer.
Start bit
Stop bit
Bit 0
Bit 1
Bit 2
Bit 3
Bit 4
Bit 5
Bit 6
Bit 7
Start bit
Bit 0
Bit 1
Bit 2
Bit 3
Bit 4
Bit 5
Bit 6
Bit 7
Stop bit
Parity
Transfer one byte without parity bit
Transfer one byte with parity bit
Notes: The main stages of a UART transmission are summarised as follows:
A data item (typically a word) is applied to the UART inputs.
A “start bit" is added to the beginning of each word to be transmitted. This bit will help synchronise the clock between sender and receiver. It is worth noting here that the transmitter and receiver clocks must not have a frequency drift by more than 10% during the transmission of the remaining bits in the word.
After the “start bit,” the remaining bits are sent, with the least significant bit (LSB) being sent first. When the entire data word has been sent, the transmitter may add a parity bit that the transmitter generates, and finally at least one stop bit is sent by the transmitter.
The receiver expects to get the stop bit at the end of the data item. If the receiver does not find the stop bit where it is supposed to, it will discard the entire word and generate a framing error when the data word is read by the processor.
If the stop bits appears, the receiver passes the data to the host.
If there is no data to transmit, the transmission line can be idle.

## Slide 7: AHB UART Peripheral
In our design, the UART peripheral consists of:
  UART transmitter, receiver
  Transmitter FIFO and receiver FIFO
  Baud rate generator
  AHB bus interface
UART
Transmitter
UART
Receiver
Baud Rate
Generator
Transmitter
FIFO
Receiver
FIFO
UART TX
UART RX
Data
Start
Done
Tick
Tick
Ready
Data
Data
Done
Data
Ready
Full
8
8
8
8
AHB
Interface
Data [31:0]
Addr [31:0]
Control [31:0]
Notes: The block diagram of the VGA peripheral is illustrated here.

## Slide 8: AHB UART Peripheral
In our design, the UART peripheral consists of:
  AHB bus interface
  It’s a bus interface which is used to communicate between the processor and the peripherals.
UART
Transmitter
UART
Receiver
Baud Rate
Generator
Transmitter
FIFO
Receiver
FIFO
UART TX
UART RX
Data
Start
Done
Tick
Tick
Ready
Data
Data
Done
Data
Ready
Full
8
8
8
8
AHB
Interface
Data [31:0]
Addr [31:0]
Control [31:0]
Notes: The AHB interface block is used to manage the flow of data and control signals from the AHB bus to the internal memory space in the UART peripheral, namely the transmit/receive FIFO memory.

## Slide 9: Baud Rate Generator
Baud rate generator
  Generate system ticks for a fixed transmission baud rate, e.g., 19200 bps byte to the receiver FIFO.
UART
Transmitter
UART
Receiver
Baud Rate
Generator
Transmitter
FIFO
Receiver
FIFO
UART TX
UART RX
Data
Start
Done
Tick
Tick
Ready
Data
Data
Done
Data
Ready
Full
8
8
8
8
AHB
Interface
Data [31:0]
Addr [31:0]
Control [31:0]
Notes: The role of the baud generator is to provide timing information for UART transmit and receive control. It takes a clock signal as an input from an on-chip clock generator. It then divides it by a divisor in the range between 1 and (216 - 1) to produce a baud clock (tick). The frequency of the baud clock is sixteen times (16×) the baud rate. This means each received or transmitted bit lasts 16 baud clock cycles (ticks). In our implementation, the baud generator contains free-running counters that generate a baud rate of 19200 based on 50MHz system clock.

## Slide 10: UART Transmitter
  Reads data (in byte) from the transmitter FIFO
  Converts a single byte data to sequential bits
  Sends bits to the tx pin, clocked in a fixed rate provided from the baud generator
UART
Transmitter
UART
Receiver
Baud Rate
Generator
Transmitter
FIFO
Receiver
FIFO
UART TX
UART RX
Data
Start
Done
Tick
Tick
Ready
Data
Data
Done
Data
Ready
Full
8
8
8
8
AHB
Interface
Data [31:0]
Addr [31:0]
Control [31:0]
Notes: The UART transmitter performs parallel-to-serial conversion on the data read from the transmitter FIFO. It then outputs the serial bit stream beginning with a start bit, data bits (with the LSB first), followed by the parity bit (if used), and then the stop bits. The UART transmitter uses the “done” signal to indicate that it is ready for the next character. The speed of the processor is typically much higher than the transmission time of a character through the UART. Therefore, to avoid data loss, it is important for the UART to prevent the host system from depositing new data items until previous transmissions are completed. This is achieved using a busy flag.

## Slide 11: UART Receiver
  Receives the sequential bits from the rx pin, using the clock generated from the baud generator
  Reassembles the bits to a single byte
  Writes the received byte to the receiver FIFO
UART
Transmitter
UART
Receiver
Baud Rate
Generator
Transmitter
FIFO
Receiver
FIFO
UART TX
UART RX
Data
Start
Done
Tick
Tick
Ready
Data
Data
Done
Data
Ready
Full
8
8
8
8
AHB
Interface
Data [31:0]
Addr [31:0]
Control [31:0]
Notes: The receiver tests the state of the incoming signal on each clock pulse, looking for the beginning of the start bit. If the apparent start bit lasts at least one-half of the bit time, it is valid and signals the start of a new character. If not, it is considered a spurious pulse and is ignored. After waiting a further bit time, the state of the line is again sampled and the resulting level clocked into a shift register. After the required number of bit periods for the character length (eight bits, typically) have elapsed, the contents of the shift register are made available (in parallel fashion) to the receiving system. The UART will set a flag indicating new data is available. In our implementation, the “done” signal at the output of the receiver indicates to the FIFO that a data item is available to be latched.

## Slide 12: Why Do We Need an FIFO in UART?
Transmitter FIFO
  Processor operates in a higher clock frequency, e.g., 50,000,000Hz
  UART data is transmitted in a much lower frequency, e.g., 19,200 Hz.
  If the processor waits for the UART, a large amount of time is wasted.
  Hence, FIFOs are used to improve the system efficiency.
Receiver FIFO:
  Used to give the processor more time to handle interrupt signals
A
B
C
D
E
F
Processor
A
B
C
D
E
F
Time
UART Transmitter
Processor quickly pushes data to FIFO
Processor
Now processor can do something else
UART slowly shifts data out
UART Transmitter FIFO
UART Transmitter FIFO
Notes:   In this implementation, the processor clock is 50MHZ, whereas the UART data is transmitted at a lower rate of 19,200 bps. If there was no transmitter FIFO, the processor would have to wait a long time for the UART to finish the transmission of each data item before it can deposit a new piece of data. The transmitter FIFO allows the processor to deposit several data items in the FIFO memory to be transmitted later on. This improves system efficiency. It is worth noting here that in principle, we can design a UART without a receiver FIFO, but the majority of UART designs have an FIFO buffer memory that sits between the receiver shift register and the host system interface. This allows the host processor more time to handle an interrupt signal from the UART.

## Slide 13: FIFO Implementation
An FIFO is usually implemented on a dual-port memory, as one port is for reading and the other is for writing.
FIFO
Dual Port Memory
Data In
Data Out
FIFO Full
FIFO Empty
FIFO Almost Full
FIFO Almost Empty
Notes: For FIFOs of non-trivial size, a dual-port RAM is usually used, where one port is dedicated to writing and the other to reading. Additional flags are used to indicate the status of the FIFO. These are summarized as follows:
FIFO Full: All memory space is used; hence, no more data can be written
FIFO Empty: No data in the memory; thus, no more data can be read
Some FIFOs also provide half full/empty signals

## Slide 14: Memory Space
The memory space is allocated as follows:
Peripheral | Base address | End address | Size
MEM | 0x0000_0000 | 0x0FFF_FFFF | 16MB
VGA | 0x5000_0000 | 0x50FF_FFFF | 16MB
UART | 0x5100_0000 | 0x51FF_FFFF | 16MB
Arm Cortex-M0
Processor
BRAM
System on Chip
Arm AMBA 3 AHB-Lite System Bus
32-bit Address Bus
32-bit Data Bus
Control Signals
VGA
Peripheral
Monitor
UART
Peripheral
To Host
Notes: Once the design of the UART peripheral is finished and its behavior is verified through digital simulations, it can be integrated with the SoC design we have already implemented in the previous labs. Our example SoC design will now have three peripherals, as shown here. Each of these needs to have its own memory space. The table in this slide shows the base and end addresses allocated to each peripheral.

## Slide 15: Memory Space
The UART peripheral should have at least two registers
  Data register
  Used for both input and output data
  FIFO status register
  Bit0: Rx FIFO Empty
  If empty, processor cannot read from the FIFO.
  Bit1: Tx FIFO Full
  If full, processor has to wait before writing to the FIFO.
Register | Base address | Size
Data | 0x5100_0000 | 4 Byte
FIFO status | 0x5100_0004 | 4 Byte
Notes:     The internal memory space of the UART peripheral is divided into two regions: a data register and an FIFO status register. The data register is a 32-bit word (four byte) space used for both input and output data. The FIFO status register also occupies a 4-byte space in the memory and it stores two flags: Rx FIFO Empty and Tx FIFO Full. If the Rx FIFO Empty is asserted, it means the processor cannot read from the FIFO. If Tx FIFO Full is asserted, the processor has to wait before writing to the FIFO.